## Slide 1
Wel-Come

## Slide 2
Dr. Dnyandev. N. Zambare M. Sc. Ph. D
Associate Professor
Department of chemistry
Kisan Veer Mahavidyalaya, Wai.
Dist- Satara pin- 412803
Mob. no.-9890891947

## Slide 3: Chapter 1. Manufacture of Heavy Chemicals (8)
Contents …
1.1 Introduction
1.2 Manufacture of Ammonia (NH3)
i. Physico-chemical principles
ii. Manufacture by Haber’s process
1.3 Manufacture of Sulphuric acid (H2SO4)
i. Physico-chemical principles
ii. Manufacture by Contact process
1.4 Manufacture of Nitric acid (HNO3)
i. Physico-chemical principles
ii. Manufacture by Ostwald’s (Ammonia oxidation process)
1.5 Manufacture of Sodium carbonate (Washing soda) (Na2CO3)
i. Physico-chemical principles
ii. Manufacture by Solvay process

## Slide 4: .1 Introduction (General Account)
1.1 Introduction:
Industrial chemistry is the branch of chemistry which deals with the preparation of various chemicals on a large scale.
The chemicals which are manufactured and consumed on commercial scale are generally known as the heavy chemicals.
The rate of a chemical reaction depends on several factors such as temperature, pressure (of the gaseous reactants), concentration and use of catalyst.

## Slide 5: :
This process was developed by Fritz Haber and Carl Bosch (German Chemists during 1904 to 1908), and therefore known as Haber Bosch process.
i. Physico-chemical principles
  The key reaction of Haber's process is
N2 (g) + 3H2 (g) → 2NH3 (g) +100 kJ ....(1)
      1 vol 3vols 2 vols
(a) Effect of Concentration:
By applying Law of Mass action to reaction (1) the equilibrium constant, Kc (for molar concentrations) is:
to get good yield of NH3, concentration of both N2 and H2 should be increased
1.2 Manufacture of Ammonia (NH3)
i. Physico-chemical principles
ii. Manufacture by Haber’s process

## Slide 6: (b) Effect of Temperature:
N2 (g) + 3 H2 (g)→ 2 NH3 (g) + 100 kJ
Since the reaction is reversible and exothermic, the decrease in temperature should favour the formation of ammonia.
The effect of temperature on ammonia synthesis can be ascertained from the mass law equation as given below:
Experimentally, the optimum temperature is found to be 500 - 550°C,(773 - 823 K).

## Slide 7: (c) Effect of Pressure:

## Slide 8: (c) Effect of Pressure:
At a given temperature, increase in pressure increases the yield of ammonia.
In practice, the process is carried out by applying the pressure equal to 200 atmospheres (202 x 105 Pa).

## Slide 9: (d) Effect of Catalyst: Time of Contact (Space Velocity) :
(i) Low Temperature (773 to 823 K) (500° - 550° C)
(ii) High Pressure ( 202 x 105 Pa or Nm-2) ( 200 atm.)
(iii) Concentration of N2: H21: 3
(iv) Space Velocity 600 - 1200 m3
(v) Catalyst: (Fe2O3 + Mo) or (Fe2O3 + Al2O3 + K2O).

## Slide 10: Manufacture by Haber’s process (Plant and Process):

## Slide 11
(i)Production and purification of the reacting Gases:
Nitrogen and hydrogen are the basic requirements of Haber's process. Hydrogen can be obtained from water gas (CO + H2), or from electrolysis of acidified water or from decomposition of steam or from natural gas. Nitrogen is obtained from producer gas (CO + N2) or air or from liquid air by fractional distillation.
(ii) Conversion to Ammonia:
N2+ 3 H2 → 2 NH3 + 100kJ
(iii) Liquefaction of Ammonia: This mixture is then passed through condensing coils (immersed in the refrigerated brine) where it is cooled to about −10° to −20°C (263 to 253 K). Gaseous ammonia condenses to liquid ammonia and is collected.
Working:

## Slide 12: Merits of Haber's Process:
( i) Highly pure and concentrated ammonia is obtained.
(ii) Process is cheap and economical on unit cost basis.
(iii) The working conditions being simple, the process can be carried out at any place.
(iv) With no loss, 8 to 12 % of NH3 is produced in each circulation by Haber process. In other methods, % yield of NH3 is less than 5.
World production of NH3 was 1 million tonnes per year in 1950 and it has risen to 98 million tonnes in 1988. The largest producers are Russia 27 %, China 21 %, USA 18 %, Canada 4 %, Romania 4 %, etc.

## Slide 13: Manufacture of H2SO4 by Contact process:
In a nut shell:
S(g) → SO2(g) → SO3(g) → H2S2O7(l) → 2H2SO4(l)
(Conditions to get good yield of Sulphur trioxide):
The entire success of contact process lies in the catalytic oxidation of sulphur dioxide to sulphur trioxide by atmospheric oxygen. This reaction may be represented as:
2 SO2 + O2 2 SO3 +189 kJ
2 vols 1vol 2 vols

## Slide 14: Physico-chemical principles
(i) Effect of Concentration:
In the reaction mixture proportion of nitrogen and hydrogen should be 1: 3
(b) Effect of Temperature:
N2 (g) + 3 H2 (g) 2 NH3 (g) + 100 kJ
the optimum temperature is found to be 500 - 550°C, (773 - 823 K).
The process is carried out by applying the pressure equal to 200 atmospheres (202 x 105 Pa).

## Slide 15
(c) Effect of Pressure:
Increase in pressure should lead to increase in yield of SO3 because with increase of pressure volume is found to decrease. In actual practice, all contact plants are operated at atmospheric pressure that is, without appixing any pressure or at slightly higher pressure of 1.5-1.7 atmospheres.
The conversion of SO2 to SO3 in the presence of catalyst is made of following steps :
Diffusion of reacting gases (SO2 + O2) to the surface of catalys
Adsorption of reactants at the surface of catalyst.
Formation of product (SO3) at the surface of catalyst.
Desorption of product from the surface of catalyst.
Diffusion of SO3 away from the surface of catalyst.

## Slide 16: (d) Effect of Catalyst:
Finely divided platinum is the most efficient catalyst. It is applied on several carriers such as asbestos, calcined magnesium sulphate, silica gel etc.
Asbestos fibers coated with finely divided platinum are called platinised asbestos.
Most widely used vanadium catalyst is V2O5. It is prepared in the form of pallets by igniting a mixture of zeolite (carrier) and suspension of V2O5.

## Slide 17: Manufacture by Contact process: (Plant and Process)

## Slide 18: Working:
The contact plant consists of the following parts:
(1) Pyrites Burners
(2) Purification unit : (i) Dusting Tower, (ii) Cooler (iii) Scrubber, (iv) Drying Tower, (v) Arsenic Purifier,(vi) Asbestos Filter, (vii) Testing Box or Tyndall Box.
(3) Contact Converter or Contact Tower.
(4) Absorption Tower.
The manufacture of sulphuric acid by contact process is carried out in four steps as discussed below:
1. Production of SO2,
2. Purification of reacting gases, (if pyrites are used),
3. Conversion of SO2 to SO3, and
4. Absorption of SO3 in conc. H2SO4.
Merits and Demerits of Contact Process:
Demerits:

## Slide 19: 1.4 Manufacture of Nitric acid (HNO3)
Physico-chemical principles:
(a) Effect of Concentration:
Consider the reaction:
4NH3 + 5O2 4NO + 6 H2O + 216.6 k cals
4 Vols. 5 Vols. 4 Vols 6 Vols.
(b) Effect of temperature
brings about this conversion very rapidly even at 750°-8000C.
(c) Effect of Pressure: three convenient ranges of pressure are found to be suitable.
1) A little above the atmospheric pressure,
2) The intermediate range (i.e. 3-4 atmospheres) and
3) The higher range (i.e. 7-9 atmospheres).
(d) Effect of Catalyst:
The oxidation of NH3 without a catalyst does not take place sufficiently quickly,platinum as the best catalyst

## Slide 20
Manufacture by Ostwald’s (Plant and Process):
Working:

## Slide 21: Working:
The Ostwald process is carried out in five steps.
i) Production of NH3 by Haber process:
ii) Oxidation of NH2 to NO,
iii) Oxidation of NO to NO2,
iv) Absorption of NO2 in water, and
v) Concentration of Nitric acid.
The details of working of Ostwald plant are as follows:
4 NO2 + O2 + 2H2O → 4HNO3

## Slide 22: 1.5 Manufacture of Sodium carbonate (Washing soda) (Na2CO3)
i. Physico-chemical principles:
From theoretical discussion it is clear that the Solvay process is based on the precipitation of sodium bicarbonate by the reaction between sodium chloride (brine) and ammonium bicarbonate from aqueous solution.
i.e. NaCl + NH4HCO3 → NaHCO3 +NH4Cl
Ionically, Na+ + Cl- + NH4+ + HCO3- → NaHCO3 +NH4+ + Cl-
By neglecting common ions, we get
Na+ + HCO3- → NaHCO3
Solvay pointed out that precipitation of NaHCO3 does not occur if NH2HCO3 is prepared first and followed by the addition of brine solution.

## Slide 23
Thus NH4HCO3 is the most soluble while NaHCO3 is the least soluble at 300C.
Therefore NaHCO3 is quantitatively precipitated out in the presence of braine at 30°C, due to common ion effect of Na+ ions (from NaC1) and HCO3- ions (which are obtained by passing CO2 through solution).
The possible reactions are:
i) NH3 + H2O → NH3.H2O i.e NH4OH
NH4OH → NH4+ + OH–
ii) CO2 + H2O → H2CO3
H2CO3 → H+ + HCO3-
iii) CO2 + OH– → HCO3-
iv) NaCl+ H2O → Na+ (aq) + Cl-(aq) (Ionisation)
Thus the net reaction is:
v) Na+ + Cl- + NH4+ + HCO3- → NaHCO3 +NH4+ + Cl-
i.e. Na+ + HCO3- → NaHCO3

## Slide 24: Conclusion:
To get good yield of NaHCO3, the following conditions have to be established.
Saturated brine solution to be used to get high initial concentration of Na+ ions.
High concentration of NH3 is needed to get higher amount of NH4HCO3 that gives high concentration of HCO3-.
Working temperature should be as low as possible to decrease the solubility product of NaHCO3.
Ammonia should be first absorbed in brine and then CO2 is to be passed in
Thus good yield of NaHCO3 gives better yield of Na2CO3.
The Solution is filtered and NaHCO3 is separated. It is dried and ignited to get anhydrous sodium carbonate called soda ash.
2NaHCO3Na2CO3 + H2O+ CO2

## Slide 25: Manufacture by Solvay process (Plant and Process):

## Slide 26: Working:For Solvay process,
(i)Purification of Brine and Saturation of Brine with Ammonia:
NH3 + H2O + CO2 → ( NH4)2CO3
CaCl2 + (NH4)2CO3 → CaCO3 + 2NH4Cl
MgCl2 + ( NH4)2CO3 → MgCO3 +2NH4Cl
(ii) Carbonation:
The reactions occurring in carbonation tower are as follows:
NH3 + H2O + CO2 + NaCl → NaHCO3 +NH4Cl
Or NH4HCO3 + NaCl → NaHCO3 +NH4Cl
Ironically NH4+ + HCO3- + Na+ + Cl- → NaHCO3 +NH4+ + Cl
Discarding the common, we get;
Na+ + HCO3- → NaHCO3
(iii) Filtration: ions
The solution collected at the base of the carbons ting tower is passed through a vacuum filter of a continuous rotary type. Sodium bicarbonate is separated out while the mother liquor containing NH4Cl and a little NH4HCO3 is pumped up to the top of ammonia recovery tower to recover NH3.

## Slide 27
iv) Calcination:
Sodium bicarbonate, thus obtained is dried and heated at about 300°C in a specially designed vessel whereby Na2CO3 is obtained.
2NaHCO3 → Na2CO3 + H2O+ CO2
(v) Generation of CO2:
Limestone is heated in lime-kiln and CO2 is produced for carbonation.
CaCO3 → CaO + CO2
(vi) Recovery of Ammonia :
Steam decomposes NH4HCO3 in the upper part of the tower.
NH4HCO3 → NH3 + H2O + CO2
Milk of lime decomposes NH4Cl in the lower part of the tower.
2 NH4Cl + Ca (OH) 2 → 2NH3 + CaCl2. + 2H2O

## Slide 28: The flow-sheet of Solvay process may be shown as follows:

## Slide 29: Advantages of Solvay Process:
(i) The raw materials required for Solvay Process are cheap and easily available on large scale.
(ii)The process is continuous and very efficient.
(iii) The process is more or less self-contained with a little loss of CO2 and NH3
(iv) The product obtained is quite cheap and highly pure.
(v) Low grade brine can be used, less raw materials are required. Power consumed is less, no investment for NH3 plant corrosion problems are less. In short, the cost of production is low and thus the process is more economical.
(vi) The co-produce to be disposed of is CaCl3 which is rather in expensive.

## Slide 30
THANK YOU